## Slide 1
AMSTer : SAR & InSAR Automated Mass processing Software for Multidimensional Time series
Nicolas d’Oreye1,2, Dominique Derauw3,4, Sergey Samsonov5,
Delphine Smittarello1, Maxime Jaspard1, Gilles Celli1
ndo@ecgs.lu
amster@ecgs.lu
1 European Centre for Geodynamics and Seismology (ECGS), 19 rue Josy Welter, L-7256 Walferdange, Luxembourg
2 National Museum of Natural History (NMNH), 19 rue Josy Welter, L-7256 Walferdange, Luxembourg
3 Centre Spatial de Liège (CSL), Avenue du Pré Aily, B-4031 Angleur, Belgium
4 SAREOS, 1 Rue des Violettes, 4557 Fraiture, Belgium
5 Canada Centre for Mapping and Earth Observation, Natural Resources Canada (NRCAN), 560 Rochester Street, Ottawa, ON K1A 0E4, Canada

## Slide 2
- Optional module for MasTer Toolbox -
Optimised pair selection
D. Smittarello1
1 European Center for Geodynamics and Seismology, Luxembourg (delphine@ecgs.lu)
AMSTer Toolbox

## Slide 3
User need to chose BTmax and BPmax
Pair Selection Principle in AMSTer Toolbox
Short baselines = better coherence Long baselines = better connectivity
BT = 12 days
BT = 72 days
BTmax = 20 days ; BPmax = 20m
BTmax = 50 days ; BPmax = 50m
BTmax = 70 days ; BPmax = 70m
BTmax = 75 days ; BPmax = 75m

## Slide 4
User need to chose BTmax and BPmax
Pair Selection Principle in AMSTer Toolbox
Best compromise depends on :
Area characteristics
Satellite orbits characteristics
Expected displacement velocity
And also :
Computational resources
Storage resources

## Slide 5
While working with :
Larger and larger databases
Limited computer resources
Why do we need optimization ?
Optimization aims at :
Saving computation time
Saving storage resources
Improve ? / Not degrade results

## Slide 6
Optimization Principle
List of SAR acquisitions (AMSTer inputs) => Prepa_msbas.sh
        List of interferograms to compute => SAR_MASS_Processing
            List of deformation maps to invert => MSBAS
                Time series (AMSTer final products)

## Slide 7
Optimization Principle
List of SAR acquisitions (AMSTer inputs) => Prepa_msbas.sh
        List of interferograms to compute => SAR_MASS_Processing
            List of deformation maps to invert => MSBAS
                Time series (AMSTer final products)
Remove from the list
Option 1
Option 2

## Slide 8
Optimization Principle
List of SAR acquisitions (AMSTer inputs) => Prepa_msbas.sh
        List of interferograms to compute => SAR_MASS_Processing
            List of deformation maps to invert => MSBAS
                Time series (AMSTer final products)
Remove from the list
Option 1
Option 2
Additional constraints :
Keep sufficient graph connectivity
Remove poor quality interferograms
Use each image as often as primary and as secondary image

## Slide 9
Baseline Plot = Graph
SAR acquisitions = nodes
Interferograms = edges
A Graph Framework
SAR 1
SAR 2
SAR 3
Interf 2-3
Interf 1-2
Interf 2-4
Interf 3-4
SAR 4
Interf 1-4
4 Nodes
5 Edges
Interf 1-3 = out of BT - BP criteria

## Slide 10
Baseline Plot = Graph
SAR acquisitions = nodes
Interferograms = edges
Node Degree = number of connected neighbors
example : SAR 2 : degree 3
SAR 3 : degree 2
A Graph Framework
SAR 1
SAR 2
SAR 3
Interf 2-3
Interf 1-2
Interf 2-4
Interf 3-4
SAR 4
Interf 1-4
4 Nodes
5 Edges
Interf 1-3 = out of BT - BP criteria

## Slide 11
Baseline Plot = Graph
SAR acquisitions = nodes
Interferograms = edges
Graph is oriented : Node In-degree = number of incoming connections
Node Out-degree = number of outcoming connections
example : SAR 2 : In-degree 1 – Out-degree 2
SAR 3 : In-degree 1 – Out-degree 1
A Graph Framework
SAR 1
SAR 2
SAR 3
Interf 2-3
Interf 1-2
Interf 2-4
Interf 3-4
SAR 4
Interf 1-4
4 Nodes
5 Edges
Interf 1-3 = out of BT - BP criteria

## Slide 12
Baseline Plot = Graph
SAR acquisitions = nodes
Interferograms = edges
Optimization
Same In-degree and Out-degree for all node : k
Find a subgraph by removing non-necessary edges
A Graph Framework
SAR 1
SAR 2
SAR 3
Interf 2-3
Interf 1-2
Interf 2-4
Interf 3-4
SAR 4
Interf 1-4
4 Nodes
5 Edges
Interf 1-3 = out of BT - BP criteria

## Slide 13
A Graph Framework
I chose k=3

## Slide 14
A Graph Framework
Which edges do I remove ?
I chose k=3
SAR i

## Slide 15
A Graph Framework
Which edges do I remove ?
I chose k=3
SAR i
In-degree = 3
3=k
OK

## Slide 16
A Graph Framework
Which edges do I remove ?
I chose k=3
SAR i
In-degree = 3
3=k
OK
Out-degree = 5
5>k
Remove 2 edges…

## Slide 17
A Graph Framework
Which edges do I remove ?
I chose k=3
SAR i
In-degree = 3
3=k
OK
Out-degree = 5
5>k
Remove 2 edges…
ID=4>k
Removable ?
YES

## Slide 18
A Graph Framework
Which edges do I remove ?
I chose k=3
SAR i
In-degree = 3
3=k
OK
Out-degree = 5
5>k
Remove 2 edges…
ID=4>k
Removable ?
YES
No
ID=3=k

## Slide 19
A Graph Framework
Which edges do I remove ?
I chose k=3
SAR i
In-degree = 3
3=k
OK
Out-degree = 5
5>k
Remove 2 edges…
ID=5>k
ID=1<k
ID=4>k
ID=3=k
ID=4>k
Removable ?
YES
YES
YES
No
No
… among 3 removable

## Slide 20
A Graph Framework
Which edges do I remove ?
I chose k=3
SAR i
In-degree = 3
3=k
OK
Out-degree = 5
5>k
Remove 2 edges…
=> Need for an additional criteria
ID=5>k
ID=1<k
ID=4>k
ID=3=k
ID=4>k
Removable ?
YES
YES
YES
No
No
… among 3 removable

## Slide 21
Coherence
Weighted Graph
Give a weight to each edge
Sort removable edges
Remove edge with the lowest weight
Coherence Proxy
Advantages
Inconvenient
Remove in priority the poorly coherent interferograms
Need to compute the coherence of each pair
No need to compute the coherence of all possible pairs
Need correct calibration

## Slide 22
Algorithm workflow
1) Create an oriented graph
2) Compute weight of each edge
3) Compute in-degree and out-degree of each node
4) For each node:
5) Compute number of edges to remove
If needed :
6) Compute number of removable edges
If possible :
7) Sort removable edges according to their weight
8) Remove edges
9) Update nodes’ degrees
end
end
End
10) Save optimized list of edges

## Slide 23
Coherence proxy
3 main causes of coherence loss
- Temporal decorrelation =>
- Spatial decorrelation =>
- Seasonal decorrelation=>
a, b and c are inverted using a calibration subset of coherence values for a list of pairs.

## Slide 24
Coherence proxy
Seasonal contribution

## Slide 25
Coherence proxy
Temporal contribution

## Slide 26
Coherence proxy
Temporal contribution
Spatial contribution

## Slide 27
Coherence proxy
Temporal contribution

## Slide 28
Coherence proxy
Spatial contribution

## Slide 29
Coherence proxy
Coherence Vs Coherence Proxy
a, b and c are inverted using a calibration subset of coherence values for a list of pairs.

## Slide 30
Some results

## Slide 31
Some results

## Slide 32
Some results

## Slide 33
The optimization toolbox practically
Exercise part 1: Install
Copy optimtoolbox.zip in $HOME/SAR/AMSTer
Open a terminal :
cd $HOME/SAR/AMSTer
unzip optimtoolbox.zip
chmod u+x $HOME/SAR/AMSTer/optimtoolbox/*.py
chmod u+x $HOME/SAR/AMSTer/optimtoolbox/*.sh
cd
edit .bashrc
Add line :
PATH=$PATH:$HOME/SAR/AMSTer/optimtoolbox
Save and quit text editor
In terminal :
source .bashrc
Already done if installation performed with AMSTer_install.sh

## Slide 34
The optimization toolbox practically
Exercise part 2: How to use
- Prepare a kml defining your calibration ROI in $PATH_1650/kml/ARGENTINA/Domuyo_Edifice.kml
- Prepare Coherence table calibration
cd $PATH_3601/SAR_MASSPROCESS/S1/ARG_DOMU_LAGUNA_A_18_SAMPLE/…
…SMNoCrop_SM_20180512_Zoom1_ML4/Geocoded/Coh
Baseline_Coh_Table.sh $PATH_1650/kml/ARGENTINA/Domuyo_Edifice.kml
Output is a text file in …/Geocoded/Coh/Baseline_Coh_Table_Domuyo_Edifice.kml.txt

## Slide 35
The optimization toolbox practically
Exercise part 2: How to use
Optimize Pair table
cd $PATH_1650/SAR_SM/MSBAS/ARGENTINE/set1
Check if table.orig already exists
Option 1 : Run using coherence values (4 arguments – same pairs in both tables)
Run_optim_module.sh $PATH_1650/SAR_SM/MSBAS/…/seti/table_0_BP_0_BT.txt
$PATH_3601/SAR_MASSPROCESS/…/Geocoded/Coh/Baseline_Coh_Table_kml.txt optimdegree coh_thres
Example :
Run_optim_module.sh $PATH_1650/SAR_SM/MSBAS/ARGENTINE/set1/table_0_20_0_450.txt_For_Optim.txt
$PATH_3601/SAR_MASSPROCESS/S1/ARG_DOMU_LAGUNA_A_18_SAMPLE/SMNoCrop_SM_20180512_Zoom1_ML4…
…/Geocoded/Coh/Baseline_Coh_Table_Domuyo_Edifice.kml.txt 3 0
Optimize Pair table
Output are textfiles in $PATH_1650/SAR_SM/MSBAS/ARGENTINE/set1/
table_0_20_0_450_listPR2rm4optim_3_th0.txt
table_0_20_0_450_listPR2rm4optim_3_th0_optimized.txt
table_0_20_0_450_orig.txt

## Slide 36
The optimization toolbox practically
Exercise part 2: How to use
Optimize Pair table
cd $PATH_1650/SAR_SM/MSBAS/ARGENTINE/set1
Check if table.orig already exists
Option 2 : Run using coherence proxy (10 arguments)
Run_optim_module.sh $PATH_1650/SAR_SM/MSBAS/…/seti/table_0_20_0_450.txt
$PATH_3601/SAR_MASSPROCESS/…/Geocoded/Coh/Baseline_Coh_Table_.kml.txt optimdegree DOYlow Mxc Mnc coh_thres
Example :
Run_optim_module.sh $PATH_1650/SAR_SM/MSBAS/ARGENTINE/set1/table_0_20_0_450.txt
$PATH_3601/SAR_MASSPROCESS/S1/ARG_DOMU_LAGUNA_A_18_SAMPLE/SMNoCrop_SM_20180512_Zoom1_ML4…
…/Geocoded/Coh/Baseline_Coh_Table_Domuyo_Edifice.kml.txt 3 230 1 0.0125 0.02 0.72 0.22 0
Optimize Pair table
Output are textfiles in $PATH_1650/SAR_SM/MSBAS/ARGENTINE/set1/
table_0_20_0_450_listPR2rm4optim_3_th0.txt
table_0_20_0_450_listPR2rm4optim_3_th0_optimized.txt
table_0_20_0_450_orig.txt

## Slide 37
The optimization toolbox practically
Exercise part 2: How to use
Prepare MSBAS
  cd $PATH_3602/MSBAS/_Argentina_S1_20m_450days
If not already done : build_header_msbas_criteria.sh
Save a copy of DefoInterpolx2Detrend1.txt
cp DefoInterpolx2Detrend1.txt DefoInterpolx2Detrend1_orig.txt
For each set of interest (here only set 1) :
Remove_Pairs_From_BaselinePlotOptimisation.sh DefoInterpolx2Detrend1 $PATH_1650/SAR_SM/MSBAS/ARGENTINE/set1/table_0_20_0_450_listPR2rm4optim_3_th0.txt
Output is a text file DefoInterpolx2Detrend1_Optimized_TABLE.txt_RUNTIME.txt
To run msbas without optimization :
cp DefoInterpolx2Detrend1_orig.txt DefoInterpolx2Detrend1.txt
To run msbas with optimized table :
cp DefoInterpolx2Detrend1_Optimized_table_0_20_0_450_listPR2rm4optim_3_th0.txt_05_16_2023_13h43m.txt DefoInterpolx2Detrend1.txt
Update header.txt : here only one set, comment line for set 2
Launch : MSBAS.sh _set1_afteroptim
cd zz_LOS_set1_afteroptim
Visualization : PlotTS.sh 2851 2696 3050 2700 -f -r -t or open maps in QGIS

## Slide 38
The optimization toolbox practically - Results
No Optim.
After Optim.
Difference